## Slide 1
client process
1 thread
component diagram
server process
Server instance
1 thread
1 thread
client process
1 thread
socket communication
Local / TCP
socket communication
Local / TCP
client
instance
client
instance
1 thread
client
instance
client
instance
ImmSocketService
1 thread
ImmSocketService
CImmSocketServer
CImmSocketClient
Managing client tables
Local / TCP
config
client
tables
Connection management with server
Connection management with client
Send and receive data
Local / TCP
config
1 thread per 1 client.
manage it by associating with fd.
In multithreading instance will be shared. Processing is exclusive every transmission.

## Slide 2
CImmSocketServer
CWorkerThread
CImmSocketClient
1
*
<<interface>>
CImmSocketCLient::
IPacketHandler
CPacketHandler
User 実装クラス
Request/Reply/Notifyのハンドリング
onHandleRequest
onHandleReply
onHandleNotify
1
0..1
CMessage
CAsyncProcProxy
CAsyncProcProxy::
CProxyThread
1
1
1
1..*
Class
diagram
1
1

## Slide 3
Command
Data
1byte
1byte
1byte
1byte
n byte
(255以内)
ID
SOH
EOT
Type
1byte
Size
1byte
Size
Data
1byte
n byte
(渡す必要あれば249byte以内で)
packet format
1byte
Reserve
1byte
Reserve
1byte
Reserve
1byte
Reserve
REQUEST
REPLY
NOTIFY
通信ID
Socket通信層
namespace ImmSocket
(libimmsocket.so)
ユーザアプリ/MW
Request/Reply/Notify メッセージ通信層
namespace ImmSocketService
(libimmsocketservice.so)
Start of heading
end of transfer
CMessage::sendRequest*
CMessage:: sendReply*
CMessage:: sendNotify
bool sendRequestSync (uint8_t command, uint8_t *pData, int size);
自由に定義
※データのシリアライズ必要あればユーザ側で実装する